ARENA（L）  SHOWER ENCLOSURE

Installation Manual

Ⅰ、Usage tool：

driller       pencil          wrench     tape measure    hammer

spirit level        screwdriver        small wood block

Ⅱ、Spare parts list：

1. Waterproof  1,       2. Moving glass 1,       3. Sealant 4,        4.Wall plug 10,

5.ST5×35 Screw 8/ST4×20 Screw 2 ,    6. Bottom sealant waterproof 1,

7. Magnetic plastic 2,           8. Fixed glass 2,                 9. Wall profile 2,

10. Bracket 2,        11. Handle 1,                         12. Hinge 2

13.Defense water piece 1   14. Profile waterproof in base 1     15. 90 defense water picec1

Ⅲ、Please check the quantity and quality of square parts before install, if you have any inquiry about it please contact our company or dealer without any hesitate, you will get satisfied reply soon!

picture 1

Ⅴ、Installation Process：

1．After measure the trim size, draw a vertical line, use an impact drill with diameter of ф6mm

to make a stiletto, put into the wall plug. Screw tight with the M5×35 stud screw.

picture 2                                             picture 3

2.Put the fix glass into the wall profile, use sealant filled in and then put the fixed glass connector to

the wall by the M5×35 screw to tighten the other side, put the glass clip into the gap, then use the six corner wrench to tighten.

3. Measure the size, fix the hinge to the wall then tighten then screw the moving glass to the hinge.

4．Then put the against water magnetism rubber to the glass. (As pic 1，As pic 3)

5．After installation finished, use Silicon to seal around.

6．Please clear the frame by neutral purification after 8 hours.

Ⅵ、Please push the door slightly,don’t scratch the frame by strong and sharp material to avoid

damaging fittings.

picture 4